PUNJAB STATE ELECTRICITY BOARD

GURU GOBIND SINGH SUPER THERMAL PLANT ROOPNAGAR

Tender Notice

| Office | General Manager/GGSSTP, Roopnagar. |
| --- | --- |
| Tender Specification No. | 6881/P-II/EMP-11028 Dated: 14.3.2016 |
| Issuing Authority | General Manager/GGSSTP, Roopnagar. |
| Address: | Dy.CE/Monitoring, GGSSTP Roopnagar. |
| Place | Roopnagar. |
| Short Description | Various types of Gun Metal Valves |
| Tender publication | ON ALL INDIA BASIS |
| Eligibility Criteria | As per terms and conditions |
| 1) Starting date of Sale of Tender | at 11.00 A.M. |
| 2) Last Date for Sale of Documents | 18.4.2016 Upto 11.00 A.M. |
| 3) Last Date of Bid Submission | 18.4.2016 Upto 11.00 A.M. |
| 4) Bid Opening | 22.4.2016 at 11.30 A.M. |
| Document Cost | Rs. 500/- |
| Payment Mode | DD or Cash |
| Payment in favour of | Accounts Officer/O&M, GGSSTP, Ropar. (PUNJAB) |
| EMD | Demand Draft in favour of Accounts Officer/O&M, GGSSTP, Ropar (PUNJAB) |
| Contact | Phone No. 01881-275666 FAX No. 01881-274232 |
| Tender Details:- Sr. No. Description Qty. (Nos.) Gun Metal GLOBE VALVES, IS:778, Class-I, screwed in bonnet, inside screw, rising stem, integral seat, renewable disc, screwed female ends to IS:554, BTP. 1.5 MPA (Hyd.), S.T.P: 1.0MPA (Hyd.) of following size (Annex-I): 1 15 mm 22 2 20 mm 5 3 25 mm 8 4 40 mm 10 5 50 mm 9 6 80 mm 2 Gun Metal GATE VALVES, IS:778, Class-I, Screwed in Bonnet, inside screw, non rising stem, integral seat, Solid wedge, screwed female ends to IS:554, BTP:1.5 MPA (Hyd.), STP:1.0 MPA (Hyd.) of following size (Annex-II): 7 15 mm 46 8 20 mm 10 9 25 mm 28 10 32 mm 3 11 40 mm 10 12 50 mm 12 Gun Metal Gate Valves as per IS 778.84, Class-I, screwed in Bonnet, rising stem, solid wedge screwed female ends as per IS 554.85, Hyd. Tested to 1.5 MPA ISI marks 13 20 mm 7 Gun Metal Plug valve as per IS 778:84, Class-2 PN-15, Screwed female thread as per IS 554-85 (Parallel) and having testing pressure BTP-2.4 Mpa, Hyd & STP. 1.6 Mpa of following size: 14 15mm 4 Gun Metal vertical lift check valve as per IS – 778.84, CI-2, GM (IS 318-81 LTB2) Screwed in cover, integral seat, Cu-alloy trim, screwed female thread to IS 544-85 (Parallel) and having testing pressure BTP-2.4 Mpa, Hyd STP. 1.6 Mpa of size: 15 25mm 2 TERMS AND CONDITIONS: A set of tender documents containing detailed technical specifications, General instructions and terms & conditions can be obtained from Dy.CE/Monitoring, V&P.O. Ghanauli, GGSSTP, Roopnagar -140113 on payment of cost by cash or demand draft drawn in favour of Accounts officer/O&M, GGSSTP, Ropar payable at Ropar (PUNJAB) Tender of firms, which do not purchase the tender documents in advance, shall not be opened. All tenders must be accompanied by earnest money at the rates prescribed in the tender documents except in the case of those tenderers who are specifically exempted there under. Telegraphic / Fax quotations shall not be accepted. Negotiations shall not be held excepting with the lowest tenderer. Dy.CE/ Monitoring, For GM/GGSSTP, Roopnagar |